IPwatchD 1.2 Test Scenarios

# Interface configuration mode

## Automatic interface configuration
Configuration:	iface_configuration automatic / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / killall ipwatchd
Expected result:	IPwatchD must find all interfaces and syslog their names.
Syslog output:	ipwatchd[2758]: Found device lo / ipwatchd[2758]: Found device eth0 / ipwatchd[2759]: IPwatchD started / ipwatchd[2759]: Entering pcap loop / ipwatchd[2759]: Received signal 15 / ipwatchd[2759]: IPwatchD stopped

## Manual interface configuration
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / killall ipwatchd
Expected result:	IPwatchD must find only interfaces specified in configuration and syslog their names.
Syslog output:	ipwatchd[3092]: Found device eth0 / ipwatchd[3093]: IPwatchD started / ipwatchd[3093]: Entering pcap loop / ipwatchd[3093]: Received signal 15 / ipwatchd[3093]: IPwatchD stopped

## Manual interface configuration with non-existing device
Configuration:	iface_configuration manual / iface eth0 passive / iface non0 passive / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -d -c /etc/ipwatchd.conf
Expected result:	IPwatchD cannot start.
Syslog output:	ipwatchd[3085]: Found device eth0 / ipwatchd[3085]: IPwatchD is unable to work with device "non0" / ipwatchd[3085]: Unable to read configuration file

## Manual interface configuration with no devices specified
Configuration:	iface_configuration manual / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -d -c /etc/ipwatchd.conf
Expected result:	IPwatchD cannot start.
Syslog output:	ipwatchd[3195]: No interfaces specified in configuration file / ipwatchd[3195]: Unable to read configuration file

# Defend interval

## Defend interval with value 0
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 0 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least two conflicts must be detected and user-defined script must be executed for each conflict.
Syslog output:	ipwatchd[3449]: Found interface eth0 / ipwatchd[3449]: IPwatchD started / ipwatchd[3449]: Entering pcap loop / ipwatchd[3449]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3449]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3449]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[3449]: Running user-defined script: /usr/sbin/ipwatchd-script "eth0" "192.168.137.137" "0:c:29:45:9f:7f" / ipwatchd[3449]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3449]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3449]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[3449]: Running user-defined script: /usr/sbin/ipwatchd-script "eth0" "192.168.137.137" "0:c:29:45:9f:7f" / ipwatchd[3449]: Received signal 15 / ipwatchd[3449]: IPwatchD stopped

## Defend interval with value 10
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least two conflicts must be detected but user-defined script must run only once.
Syslog output:	ipwatchd[3485]: Found interface eth0 / ipwatchd[3485]: IPwatchD started / ipwatchd[3485]: Entering pcap loop / ipwatchd[3485]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3485]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3485]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[3485]: Running user-defined script: /usr/sbin/ipwatchd-script "eth0" "192.168.137.137" "0:c:29:45:9f:7f" / ipwatchd[3485]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3485]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3485]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - no action taken because this happened within the defend interval / ipwatchd[3485]: Received signal 15 / ipwatchd[3485]: IPwatchD stopped

# User-defined script

## Configuration without user-defined script
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 10 / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least one conflict must be detected and user-defined script cannot be executed.
Syslog output:	ipwatchd[3892]: Found device eth0 / ipwatchd[3893]: IPwatchD started / ipwatchd[3893]: Entering pcap loop / ipwatchd[3893]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3893]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3893]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[3893]: No user-defined script specified / ipwatchd[3893]: Received signal 15 / ipwatchd[3893]: IPwatchD stopped

## Configuration with user-defined script
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 10 / user_script /usr/sbin/ipwatchd-script / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least one conflict must be detected and user-defined script must be executed.
Syslog output:	ipwatchd[3920]: Found device eth0 / ipwatchd[3921]: IPwatchD started / ipwatchd[3921]: Entering pcap loop / ipwatchd[3921]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[3921]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[3921]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[3921]: Running user-defined script: /usr/sbin/ipwatchd-script "eth0" "192.168.137.137" "0:c:29:45:9f:7f" / ipwatchd[3921]: Received signal 15 / ipwatchd[3921]: IPwatchD stopped

# Protection modes

## Active protection mode
Configuration:	iface_configuration manual / iface eth0 active / defend_interval 10 / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least one conflict must be detected and ARP reply must be sent.
Syslog output:	ipwatchd[2691]: Found device eth0 / ipwatchd[2692]: IPwatchD started / ipwatchd[2692]: Entering pcap loop / ipwatchd[2692]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[2692]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[2692]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - active mode - reply sent / ipwatchd[2692]: Packet with size of 42 bytes sent / ipwatchd[2692]: Packet with size of 42 bytes sent / ipwatchd[2692]: No user-defined script specified / ipwatchd[2692]: Received signal 15 / ipwatchd[2692]: IPwatchD stopped

## Passive protection mode
Configuration:	iface_configuration manual / iface eth0 passive / defend_interval 10 / syslog_facility daemon
Actions:	/usr/sbin/ipwatchd -t -d -c /etc/ipwatchd.conf && \ / sleep 1 && \ / arping -U -c 1 -I eth0 192.168.137.137 && \ / sleep 1 && \ / killall ipwatchd
Expected result:	At least one conflict must be detected and ARP reply cannot be sent.
Syslog output:	ipwatchd[2724]: Found device eth0 / ipwatchd[2725]: IPwatchD started / ipwatchd[2725]: Entering pcap loop / ipwatchd[2725]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[2725]: Device info: eth0 192.168.137.137-0:c:29:45:9f:7f / ipwatchd[2725]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 192.168.137.137 set on interface eth0 - passive mode - reply not sent / ipwatchd[2725]: No user-defined script specified / ipwatchd[2725]: Received signal 15 / ipwatchd[2725]: IPwatchD stopped

# Desktop notification support
## GNOME
Configuration:	Default
Actions:	Build and install ipwatchd and ipwd-gnotify / Edit /etc/init.d/ipwatchd and change daemon arguments to: / DAEMON_ARGS="-t -d -c /etc/ipwatchd.conf" / Make sure IPwatchD is running in your runlevel. If needed run: / update-rc.d ipwatchd defaults / Restart OS and login into GNOME / To cause IP conflict execute: / arping -U -c 1 -I eth0 192.168.137.137
Expected result:	Notification bubble must be displayed after arping.
Syslog output:	ipwatchd[1640]: Received ARP packet: S:192.168.137.137-0:c:29:45:9f:7f D:192.168.137.137-ff:ff:ff:ff:ff:ff / ipwatchd[1640]: Device info: lo 127.0.0.1-0:0:0:0:0:0 / ipwatchd[1640]: MAC address 0:c:29:45:9f:7f causes IP conflict with address 127.0.0.1 set on interface lo - passive mode - reply not sent / ipwatchd[1640]: Running user-defined script: /usr/sbin/ipwatchd-script "lo" "127.0.0.1" "0:c:29:45:9f:7f"